## Slide 1: Inverse Kinematics
Using Trigonometry

## Slide 2: Inverse Kinematics using Trigonometry
X
Z
θ1
θ3
h
L3
L2
P(x,y,z)
θ2
Y
The figure illustrates a 3R-3D Planar Robot Manipulator capable of reaching any point P(x,y,z) in a XYZ-workspace
In inverse kinematics, the goal is to determine the joint angles (θ1,θ2,θ3) for a given end-effector position P(x,y,z)
This problem cannot be solved using a purely 2D geometric approach. Therefore, the manipulator is conceptually decomposed into two view ports, similar to the forward kinematics formulation:
Top View - captures rotational motion
Side View - captures movement of other links

## Slide 3: Top View
X
Y
P(x,y)
θ1
d
y
x
For inverse kinematics, we need to solve for the top view first
From the top view, we simply see how the arm is rotated around the base and how the projected length d spreads into the X and Y directions.
Considering P(x, y) are given, we get,
tanθ1 = y / x
∴ θ1 = tan-1(y / x)
For further calculations in the side view, we need to calculate the value of d.
d = √(x2 + y2)

## Slide 4: Side View
In side view, d (the projection of the arm) becomes the value of x.
In the modified side-view formation, θ2 is divided into two parts.
θ2 = ∠CAP (θ’2) + ∠PAB (θ’’2)
Now we need to separately calculate θ’2 and θ’’2
X
Z
θ3
h
L3
L2
P(d,z)
θ2
d (projection)
A
C
B
θ’2
θ’’2

## Slide 5: Side View
From ⃤ APB, we get
X
Z
θ3
h
L3
L2
P(d,z)
θ2
d (projection)
A
C
B
θ’2
θ’’2
θ’’2 = tan-1( )
z - h
d
θ’’2 = tan-1( )
z - h
√(x2 + y2)
A
P
B
θ’’2
and,
d
z-h
AP2 = d2 + (z-h)2
AP2 = (√(x2 + y2))2 + (z-h)2
AP = √ (x2 + y2+ (z-h)2)

## Slide 6: Side View
From ⃤ CAP, we get
X
Z
θ3
h
L3
L2
P(d,z)
θ2
d (projection)
A
C
B
θ’2
θ’’2
cos θ’2 = (cosine rule)
AC2 + AP2 - CP2
2. AC . AP
A
P
C
Finally,
θ’2
θ’2= cos-1
L22 + AP2 - L32
2. L2. AP
θ2 = θ’2 + θ’’2
θ2 =
cos-1( ) +
L22 + AP2 - L32
2. L2. AP
tan-1( )
z - h
√(x2 + y2)

## Slide 7: Side View
From ⃤ CAP, we also get
X
Z
θ3
h
L3
L2
P(d,z)
θ2
d (projection)
A
C
B
θ’2
θ’’2
cos θ3 = (cosine rule)
AC2 + CP2 - AP2
2. AC . CP
A
P
C
θ3 = cos-1
L22 + L32 - AP2
2. L2. L3
θ3
Results:
θ1 = tan-1(y / x)
θ2 =
cos-1( ) +
L22 + AP2 - L32
2. L2. AP
tan-1( )
z - h
√(x2 + y2)
θ3 = cos-1
L22 + L32 - AP2
2. L2. L3

## Slide 8: Inverse Kinematics using Trigonometry [Extension]
X
Z
θ1
θ3
h
L3
L2
P(x,y,z)
θ2
Y
θ1 = tan-1(y / x) or, (90 - tan-1(y / x)
θ2 =
cos-1( ) +
L22 + AP2 - L32
2. L2. AP
tan-1( )
z - h
√(x2 + y2)
θ3 = 180 - cos-1
L22 + L32 - AP2
2. L2. L3
Here,
AP2 = (√(x2 + y2))2 + (z-h)2